Air Conditioning System
Arduino IoT Final Project Assignment

Author: Filip Kolev

# Project Description
The project represents an air conditioning system which can be controlled remotely.

Locally, there is a Genuino Uno board which reads the current temperature from a sensor and sends it to an ESP-8266 chip to upload in Adafruit IO. The ESP chip reads two feeds from Adafruit – the requested temperature and whether the system is on or off. The local Genuino is responsible for maintaining a temperature close to the requested value if the system is on by turning on a motor (fan) to reduce the temperature or a heater to increase it (not implemented due to lack of hardware).

On the remote side there is one Genuino Uno, one ESP chip, 6 LEDs, a piezo buzzer and an IR reader. The Genuino reads the IR sensor to determine the temperature the user has requested (this is done via a remote control). The reading is sent to the ESP to upload to Adafruit IO. A green LED is on when the system is turned on in Adafruit; attempting to use the system when it is off will produce a sound notification from the piezo buzzer. The other 5 LEDs are used to show the user the current temperature which she’s requesting – each LED represents a power of two to be added up; with 5 LEDs this means a 5-bit binary number for a range of 000002 – 111112 which translates to 0 – 31 degrees C°. The user uses an up and down buttons to increase/decrease the requested temperature and an OK button to confirm her choice (this causes the Genuino to send the reading to the ESP). LEDs flash while user selects, then stay on when OK is pressed. Trying to increase the temperature above the maximum of 31 or to decrease it below the minimum of 0 will cause a sound alert by the piezo buzzer.

Used hardware: 6 leds, Arduino, ESP-8266, heat and humidity sensor, motor, relay module, remote, IR sensor, piezo buzzer, jumpers, ....

# Communication protocol between Genuino and ESP-8266
## Master and slave
The Genuino Uno boards play the role of Master devices. Their role is to handle any condition which is not expected by the slave devices, e.g. receiving a message for an unknown recipient. Anything that the slaves are not supposed to do (or don’t know how to do) is sent to the Master.

## Message content
bytes (7+ required per message):
0 – start symbol
1 – from (0 – Arduino, 1 – ESP, other – unknown)
2 – to (0 – Arduino, 2 – ESP, other – unknown)
3 – number of bytes to follow (data)
4+ - data
n-2 – end symbol
n-1 – checksum

## Registering devices
Each device keeps a list of devices it can communicate directly with. The registration process is a three-way handshake.

## Handling of messages
Messages not for the receiving device are forwarded – 1) to the recipient if the recipient is registered with the receiver; 2) to the master if it is not (“if unsure, let the boss figure it out”).
Messages for the receiving device are handled by it. If the sender is not registered, an error is logged and the message data is disregarded (“only talk to your friends”).