Used hardware: 6 leds, Arduino, ESP, heat and humidity sensor, motor, relay module, remote, IR diode, piezo buzzer, jumpers.

Air conditioning system
In Adafruit IO – user can turn on or off the system.
A green LED shows whether system is on (controlled by ESP which requests on/off data).
Heat and humidity readings sent every minute to Adafruit (controlled by ESP).
Using remote control, user can control temperature – between 0 and 30 degrees C. (controlled by Arduino, then sent to ESP to forward to Adafruit).
5 LEDs show the requested temperature – binary representation (controlled by Arduino).
ESP sends the requested temperature to Adafruit if system is on.
Motor is turned on if temperature is higher than requested (controlled by Arduino based on data received from ESP). The bigger the difference, the faster the rotation speed.
Piezo buzzer warns if user tries to use system when off (controlled by Arduino).
Remote control – press up/down to select temperature, press OK to send. LEDs flash while user selects, then stay on when OK is pressed.
Hot/cold?

Communication protocol between Arduino and ESP.
bytes (7+ required per message):
0 – start symbol
1 – from (0 – Arduino, 1 – ESP, other – unknown)
2 – to (0 – Arduino, 2 – ESP, other – unknown)
3 – number of bytes to follow (data)
4+ - data
n-2 – end symbol
n-1 – checksum